## Slide 1
New experimental and calculated linelists for H2O – CO2 collision system: the impact on atmospheric water vapor retrievals
É. Ducreux, B. Grouiez, S. Robert, M. Lepère, B. Vispoel, R. R. Gamache, L. Régalia
ROYAL BELGIAN INSTITUTE FOR SPACE AERONOMY
New
H2O – CO2
parameters
© ESA/NASA/JAXA
Monday 10th March 2025

## Slide 2: Context: EnVision mission
Radars and spectrometers onboard
To study the evolution of the planet and its volcanic activity
A new mission to Venus
© ESA/NASA

## Slide 3: Venus and its atmosphere
Molecular species | Amount in the lower atmosphere
Carbon dioxide | 96 %
Nitrogen | 3.5 %
Sulfur dioxide | 150 ppm
Argon | 70 ppm
Carbon monoxide | 40 ppm
Water vapor | 30 ppm
Neon | 5 ppm
Carbonyl sulfide | 4 ppm
H2O will be greatly disturbed by the surrounding CO2
=> Need of appropriate spectroscopic parameters
At the surface: 93 bar and 737 K
© Pearson Edu.
Taylor et al., Space Sci. Rev (2018)

## Slide 4: VenSpec-H instrument details
Need to look through the clouds
  Infrared
  Only during the night
  Only through ‘Atmospheric transparency windows’
Bézard and De Bergh, JGR (2007)
2.34 µm → from 30 km to 45 km
Spectral resolution = 0.5 cm-1
1.74 µm → from 20 km to 30 km
Spectral resolution = 0.6 cm-1
1.18 µm → from 0 km to 15 km
Spectral resolution = 0.9 cm-1

## Slide 5: Laboratory measurements
In the lab:
P, T fixed
Spectroscopic parameters ?
In the atmosphere:
Spectroscopic parameters fixed
P, T, molecular abundance ?

## Slide 6: Instrumental setup
High resolution Fourier Transform IR Spectrometer + 2-m multireflexion cell
Bruker IFS 125 HR
Spectral range: 700-33000 cm-1
MPD : 3.72 m
Resolution : 0.0024 cm-1
Beamsplitters: KBr, CaF2
Quartz vis
Detectors : HgCdTe, InSb

## Slide 7: Recorded spectra at 2.7 µm
Path length: 8 m - Iris aperture: 0.85 mm - At room temperature ~292 K
Spectral resolution: from 0.016 to 0.022 cm-1
P(H2O) = 1.5 Torr + several P(CO2) = 100, 200, 300, 500 Torr.
Ducreux et al., JQSRT (2024)
Régalia et al., JQSRT (2019)

## Slide 8: Recorded spectra at 2.34 µm
Path length: 64 m - Iris aperture: 0.85 mm - At room temperature ~297 K
Spectral resolution: 0.01 cm-1
P(H2O) = 1.0 Torr + several P(CO2) = 100, 200, 300, 500 Torr.
Ducreux et al., JQSRT (2025)
In preparation

## Slide 9: Recorded spectra at 1.18 µm
Path length: 104 m - Iris aperture: 1.00 mm - At room temperature ~295 K
Spectral resolution: 0.02 cm-1
P(H2O) = 1.0 Torr + several P(CO2) = 100, 200, 300, 500 Torr.
Ducreux et al., JQSRT (2025)
In preparation

## Slide 10: Multispectrum fitting procedure
MSF (Lyulin, Atmo. Oc. Opt. 2015): beyond-Voigt line profiles
Profiles | Parameters
Voigt | Γ0, Δ0
quadratic Speed-Dependent Voigt | Γ0, Δ0, Γ2, Δ2
Ngo et al., Ph. Trans. R. Soc. (2012)
Ngo et al., JQSRT (2013)
Considering finer effects
Residuals with W-shape using the Voigt profile
Narrowing of the water line

## Slide 11: Profiles comparison at 2.34 µm
Ducreux et al., JQSRT (2025)
In preparation

## Slide 12: CO2-collisional parameters calculations
New calculations in Venusian atmospheric windows for many transitions:
Refine the H2O-CO2 interaction potential
Semi-classic Complex Robert-Bonamy-Ma (CRBM) calculations
Robert & Bonamy, J Phys (1979) - Ma et al., JQSRT (2007)
List of CO2-collisional parameters for H2O
to simulate Venus atmosphere
Bastien Vispoel
Invited talk
Tuesday 14h00

## Slide 13: Calculations comparison
APD = 1.3 % - STD = 7.4 %
Abs. mean dev. = 0.0037 cm-1.atm-1
Ducreux et al., JQSRT (2025)
In preparation
Γ
Δ

## Slide 14: Atmospheric retrievals and radiative transfer

## Slide 15: Radiative transfer model – Asimut
Simulation of Venus atmospheric spectra from lists of calculated parameters in Voigt profile
Retrieval of the water vapor amount in the atmosphere from a spectrum
Estimate the error made using air-collisional instead of CO2-collisional parameters
Vandaele et al. (2006)
Around 2.34 µm

## Slide 16: Venus atmospheric spectra simulation
1.18 µm
0 - 15 km
P = 93 bar
T = 740 K
30 ppm H2O

## Slide 17: Venus atmospheric spectra retrievals
1.38 µm
65 - 80 km
P = 1e-02 bar
T = 220 K
5 ppm H2O

## Slide 18: Venus atmospheric spectra retrievals
1.38 µm
65 - 80 km
P = 1e-02 bar
T = 220 K
5 ppm H2O

## Slide 19: Venus atmospheric spectra retrievals
Bias = 36.63 ± 0.04 %

## Slide 20: Conclusions

## Slide 21: Conclusions
New measurements of H2O-CO2 collisional parameters
New calculations in Venus atmospheric transparency windows
Lead to significant biases in water vapor retrieved in the mesosphere
Need further investigations for the troposphere
Two papers in preparation to share both lists of line-shape parameters
To come: HDO-CO2 collisional parameters

## Slide 22
thank you! Questions?
emile.ducreux@univ-reims.fr

## Slide 23: Annexes

## Slide 24: Absorption spectrum
Beer-Lambert Law:
Line parameters:
Position σ0, Intensity S,
Half-width γ, Shift δ
Laboratory measurements to atmospheric spectra study

## Slide 25: Previous work
To insert a slide in this lay-out:
  click right
  Select “Layout”
  Select “BIRA-IASB Left banner”
Régalia et al., JQSRT (2019)
At 2.7 µm with the previous FTIR spectrometer

## Slide 26: Multispectrum fitting procedure
MFT (Plateaux et al. 2001): Voigt profile and pressure fitting
MSF (Lyulin et al. 2015): beyond-Voigt line profiles
Too weak
Saturated
Good

## Slide 27: Multispectrum fitting procedure
MSF (Lyulin, Atmo. Oc. Opt. 2015): beyond-Voigt line profiles
Profiles | Parameters
Voigt | Γ0, Δ0
Rautian | Γ0, Δ0, νVC
quadratic Speed-Dependent Voigt | Γ0, Δ0, Γ2, Δ2
quadratic Speed-Dependent Rautian | Γ0, Δ0, Γ2, Δ2, νVC
Ngo et al., Ph. Trans. R. Soc. (2012)
Ngo et al. , JQSRT (2013)
Considering finer effects
Limit cases of the Hartmann-Tran profile
Residuals with W-shape using the Voigt profile
Narrowing of the water line

## Slide 28: Water vapour adsorption
H2O adsorption in the stainless steel cell → H216O partial pressure correction
Intensities fixed at HITRAN2020 values with uncertainty < 1 %
MFT (Plateaux et al., JQSRT 2001): Voigt profile and pressure fitting
Loos et al., JQSRT (2017)
Ducreux et al., JQSRT (2024)
Before
After
Fitted pressures always under measured ones.

## Slide 29: Profiles comparison at 2.7 µm
Ducreux et al., JQSRT (2024)

## Slide 30: Literature comparison qSDV
APD = 2.9 % - STD = 5.6 %
APD = 25.2 % - STD = 59.6 %
Deichuli et al., AOO (2022a)
Γ
Γ2

## Slide 32: Venus atmospheric spectra simulation
Several atmospheric transparency windows of Venus
Comparison between air- and CO2- collisional simulated spectra

## Slide 33: Venus atmospheric spectra simulation
Simulation of Venus atmospheric spectrum using CO2-collisional parameters
Random noise added for a statistic sample of 1000 spectra
H2O retrieval on the 1000 noisy spectra using CO2-collisional parameters
H2O retrieval on the 1000 noisy spectra using air-collisional parameters
RETRIEVAL METHOD
Bias using air-collisional parameters

## Slide 34: Venus atmospheric spectra retrievals
1.18 µm
0 - 15 km

## Slide 35: Venus atmospheric spectra retrievals
Bias = 0.00 ± 0.02 %

## Slide 36: Venus atmospheric spectra retrievals
1.18 µm
0 - 15 km
P = 93 bar
T = 740 K

## Slide 37: Venus atmospheric spectra retrievals
1.18 µm
0 - 15 km
P = 93 bar
T = 740 K

## Slide 38: Venus atmospheric spectra retrievals
1.18 µm
0 - 15 km
P = 93 bar
T = 740 K

## Slide 39: Venus atmospheric spectra retrievals
1.18 µm
0 - 15 km
P = 93 bar
T = 740 K

## Slide 40: Venus atmospheric spectra retrievals
Bias = 1.61 ± 0.02 %

## Slide 41: Venus atmospheric spectra retrievals
Spectral region | Planet side | Probed altitude range | Bias ± error
1.18 µm | Nightside | 0 – 15 km | 1.61 ± 0.02 %
1.74 µm | Nightside | 20 – 30 km | -0.28 ± 0.03 %
2.34 µm | Nightside | 30 – 45 km | 1.10 ± 0.16 %
2.34 µm | Dayside | 65 – 80 km | 11.34 ± 0.23 %
1.38 µm | Dayside | 65 – 80 km | 36.63 ± 0.04 %

## Slide 42: H2O retrievals on Venus simulated spectra
No dependence VS SNR

## Slide 43: H2O retrievals on Venus simulated spectra
Dependence VS spectral resolution at 1.17 µm

## Slide 44: H2O retrievals on Venus simulated spectra
And about the old observations?